G-BPWA PA-28-161 1976

# TAKE OFF AND CLIMB

Normal, Vr = 45 - 55 KIAS, Vy = 79 KIAS,

Short field, obstacle clearance, Vr = 52 KIAS, Climb at 52 KIAS with flaps 25( past obstacle, then accelerate to 79 KIAS and retract flaps slowly.

Short field, no obstacle, Vr = 50 KIAS, after breaking ground accelerate to 79 KIAS.

Best angle climb, Vx = 63 KIAS with flaps up	En route climb speed is 87 KIAS

# FUEL

8.8 USGPH @ 2400 RPM @ 2500’ with mixture leaned for best power gives 102 KIAS.

10 USGPH @ 2550 RPM @ 2500’ with mixture leaned for best power gives 112 KIAS.

Usable fuel is 48 US Gallons.

Aircraft weighs 1495 lb; full fuel weighs 288 lb, leaving 542 lb for crew, passengers and baggage.

# APPROACH SPEEDS

Trim to 70 KIAS with flaps up, 63 KIAS with flaps 40 (

63 KIAS with 40 ( of flap for a short field landing.

# UPPER AIR WORK

Utility category - 2 020 lb:	Stalls, steep turns, lazy eights and chandelles.

# STALLING SPEEDS

At 2325 lbs:	Clean – 50 KIAS, Flaps 25 ( - 47 KIAS, Flaps 40 ( - 44 KIAS.

# GLIDE

At 73 KIAS the aircraft will glide 4 nautical miles from 2 000’ agl.

# SUCTION

5 ( 0.1 inches of mercury	www.gridline.co.uk		22-Oct-00 G-BPWA.doc