G–VECE ROBIN ALPHA 120 T – R 2120 2001

# TAKE OFF AND CLIMB

Vr = 54 kt, Vy = 75 kt		Normal take-off without flap

Vr = 54 kt, Vx = 67 kt		Normal take-off with 10 ( flap

Vr = 54 kt, Vx = 60 kt		Obstacle clearance with 10 ( flap

Soft and short field use 10 ( flap	Crosswind use 10 ( flap (demonstrated at 18 kt)

# FUEL

Usable fuel is 31 US Gallons (USG)

6.7 USGPH @ 2550 RPM @ 3000’ using best power mixture – TAS 94 kt.

5.8 USGPH @ 2400 RPM @ 3000’ using best power mixture – TAS 86 kt.

Aircraft weighs 1 217 lb, usable fuel weighs 186 lb, leaving 361 lb for crew.

# APPROACH SPEEDS

75 kt with flaps up, 62 kt with flaps down, crosswind use 10 ( flap and 70 kt + 0.5 gust speed

60 kt crossing the threshold with power on for a short field landing in smooth air

# UPPER AIR WORK

‘U’ Category 1764 lb – stalls, turns at more than 60 ( bank, lazy eights, chandelles.

# STALLING SPEEDS

Power off @ 1764 lb: 	Clean - 57 kt.  Flaps 10 ( - 54 kt.  Flaps 35 ( - 48 kt

# GLIDE

Pilot’s Operating Handbook gives 75 kt (aircraft covers 2.99 Nm from 2 000’ agl).

# SUCTION

5 ( 0.1 inches of mercury	www.gridline.co.uk 	23-Apr-05 G-VECE.doc