G–BZOY BE76

# TAKE OFF AND CLIMB

Runway checks, Vmca= 65 KIAS, Vr = 70 KIAS, 8( NU, Vtoss = 75 KIAS, Vyse = 85 KIAS, 400’ after take-off checks;

Climb 100 KIAS, 5( NU, 25”/2500 RPM, 16 USGPH, prop. synchronisation, CHT 500(  F

# FUEL

102.5 US Gallons (100 USG usable).

Aircraft weighs 2 642 lb, usable fuel weighs 600 lb, leaving 658 lb for crew and baggage.

# FLIGHT AT VARIOUS SPEEDS AND CONFIGURATIONS

S&L attitude 1( ND, 23”/2300 RPM, 12 USGPH - 140 KIAS cruise checks;

Descent airways 3( ND, 18”/2300 RPM -140 KIAS;

Holding IAP checks S&L 1(NU, 18”/2300 RPM, 10 USGPH -120 KIAS;

Initial approach 110 KIAS, 10( flap, 3( ND, 14”/2500 RPM;

Final approach 100 KIAS, u/c, 25( flap, 3( ND, 17”/2700 RPM;

Visual final 85 KIAS, full flap, power as required, max RPM;

Vat=75 KIAS, flapless 80 KIAS.

# GO AROUND

100 KIAS full power/2700 RPM, Climb attitude 8( NU, gear up and flaps up;

Above 200’ flaps up, above 400’ climb power 25”/2500 RPM - 120 KIAS, after take-off checks.

# UPPER AIR WORK AND STALLING SPEEDS

Hasell checks, Clean – min. power 70 KIAS, SSR

Approach stall with gear down, power 12-13” and full flap - 60 KIAS, SSR

ASYMMETRIC SPEEDS AND CONFIGURATIONS

Climb single engine - 85 KIAS, max. power/2700 RPM, 5( NU, gear up, flaps up, live engine cowl flaps open and dead engine cowl flaps closed;

Cruise and hold single engine - 100 KIAS, 1( NU, 21”/2400 RPM;

Intermediate descent single engine – 100 KIAS, 1( ND, 15”/2400 RPM;

Final descent single engine with 10( flap and gear down 100 KIAS full power, 1( ND, 18”-20”/2700 RPM;

Visual final approach speeds, gear down and flaps 40(, 85 KIAS, power as required/2700 RPM, cowl flaps open, Vat = 75 KIAS (Vat = 80 KIAS flapless).

BUFPLAF; Brakes, Undercarriage, Flaps, Power  25”/2500 RPM, Landing light off, Altimeters set QNH, Fuel pumps off above 500’ agl (on if remaining in circuit)

IFREDAAC; Icing, FREDA, Alternator 35A optimum and 60A maximum and cowl flaps

THAL; Track VOR set, Heading bugged, Aids SID, Level check/change;

TTT;

HASELL;

WIFREDAAC; Weather ATIS, Icing, FREDAAC;

BUMPFFFICHLAM; Landing light on, Altimiters set/DA/MDA, Landing clearance obtained;

PUFFAL; Propellers, Undercarriage, Flap 25( normal, max 10( Asymmetrical, failure flags check, Altimeters set and landing clearance obtained;

URAP; Undercarriage down, Runway clear, Approach stable, Permission clearance obtained;

Note: Reds, blues and greens checked on final.