G–BZOY BE76

# EFATO TOUCH DRILLS

MAINTAIN DIRECTIONAL CONTROL by preventing yaw and roll with rudder and aileron, maintain 6( NU;

# IDENTIFY – “Left engine failed”;

# FULL POWER RIGHT ENGINE – “Right mixture rich, right prop lever forward, right throttle forward;

# GEAR UP, FLAPS UP – “Check visually”

CONFIRM “Dead leg, dead engine, left engine failed”;

FEATHER DEAD ENGINE

“Left THROTTLE closed”………….touch drill only;

“Left PROPELLER feathered”…….touch drill only;

“Left MIXTURE ICO”………………touch drill only;

LEFT ENGINE ON FIRE?

“TRIM aircraft in pitch to 6(  NU and blue line speed 85 Knots”

Set zero thrust to simulate left propeller feathered - 12” MAP.

ENGINE FAILED IMMEDIATE ACTIONS:

“Left fuel off”………………....touch drill only;

“Left pump off”……………….touch drill only;

“Left mags off”……………….touch drill only;

“Left cowl flap closed”………action;

Follow ATC instructions and simulate PAN or MAYDAY call….NIPA.

SECURE LIVE ENGINE

Right cowl flap open, alternator charging, T’s & P’s in the green, suction five inches, squawk 7700