G–BKDI - PETIT PRINCE ROBIN DR400/120 1975

# TAKE OFF AND CLIMB

Vr = 50 - 54 kt, Vy = 75 - 80 kt		Take-off without flap

Vr = 50 - 54 kt, Vy = 75 - 80 kt		Normal take-off with 15 ( flap

Vr = 50 - 54 kt, Vx = 70 kt			Obstacle clearance with 15 ( flap

Soft and short field use 15 ( flap		Crosswind use 15 ( flap

# FUEL

Usable fuel is 29 US Gallons (USG)

6.5 USGPH @ 2600 RPM @ 2500’ using best power mixture – TAS 102 kt.

Aircraft weighs 1 219 lb, usable fuel weighs 174 lb, leaving 591 lb for crew / passengers.

# APPROACH SPEEDS

70 kt with flaps up, 60 kt with flaps down, crosswind use 15 ( flap and 65 kt

60 kt crossing the threshold with power on, for a short field landing in smooth air.

# UPPER AIR WORK

‘U’ Category 1984 lb – stalls, steep turns, lazy eights, chandelles.

# STALLING SPEEDS

Power off @ 1984 lb: 	Clean - 51 kt.  Flaps 15 ( - 48 kt.  Flaps 45 ( - 45 kt

# GLIDE

Pilot’s Operating Handbook gives 73 kt (aircraft covers 3.44 Nm from 2 000’ agl).

# SUCTION

5 ( 0.1 inches of mercury		www.gridline.co.uk 16-Jun-01 G-BKDI.doc