G-BOFW A-150M

# TAKE OFF AND CLIMB

Vr = 60 mph, Vy = 78 mph	Normal take off

Vr = 60 mph, Vx = 70 mph	Short field with flaps up.

Soft field use 10 ( flaps	Normal climb 75-85 mph.

# FUEL

4.8 USGPH @ 2500 RPM @ 2500’ with mixture leaned to peak RPM – 103 mph TAS.

5.8 USGPH @ 2650 RPM @ 2500’ with mixture leaned to peak RPM – 113 mph TAS.

Usable fuel capacity is 22.5 US Gallons.

Aircraft weighs 1 152 lb, full fuel weighs 135 lb, leaving 313 lb for crew

# APPROACH SPEEDS

80 mph with flaps up (See POH), 60-70mph with flaps down.

60mph with 40 ( flap (55 mph crossing the threshold) for a short field landing in smooth air.

# UPPER AIR WORK

Gross weight 1600 lb – stalls, loops, spins, rolls, snap rolls, immelmanns, steep turns, lazy eights and chandelles.

# STALLING SPEEDS

Power off @ 1600 lbs:	Clean – 55 mph, Flaps 20( - 49 mph, Flaps 40( - 48 mph Steep gliding turns – 63 mph

# GLIDE

At 70 MPH the aircraft will glide about 2.92 Nm from 2 000’ agl.

# SUCTION

3 – 5 inches of mercury	www.gridline.co.uk		22-Oct-00 G-BOFW.doc