G-MELT F-172H 1969

# TAKE OFF AND CLIMB

Vr = 60 mph	Vy = 80 mph	Normal Take-off

Vr =60 mph	Vx = 66 mph	Short field with flaps up

Soft field use 10 ( flap		Normal climb 80 - 90 mph.

# FUEL

At 75% power consumption is 8.5 USGPH @ 2500 RPM @ 2500’ with mixture leaned.

Usable fuel is 38 US Gallons.

Aircraft weighs 1457 lb, full fuel weighs 228 lb, leaving 615 lb for crew, passengers and baggage.

# APPROACH SPEEDS

70 - 80 mph with flaps up, 65 - 75 mph with flaps down

69 mph with 40 ( of flap for a short field landing in smooth air

# UPPER AIR WORK

Utility category - 2 000 lbs:	Stalls, spins, steep turns, lazy eights and chandelles.

# STALLING SPEEDS

Power off @ 2 300 lbs:	Clean – 57 mph, Flaps 10( - 52 mph, Flaps 40 ( - 49 mph

# GLIDE

At 80 mph the aircraft will glide 3.33 statute miles from 2 000’ agl.

# SUCTION

4.6 – 5.4 inches of mercury	www.gridline.co.uk		22-Oct-00 G-MELT.doc