G–REDB C 310Q

# TAKE OFF AND CLIMB

Vr = 90 MPH, Vxse = 108 MPH	Normal take-off with 0 ( flap

Vr = 90 MPH, Vyse = 116 MPH	Flaps up (blue radial)

Vr = 89 MPH, Vx = 89 MPH		Obstacle clearance with 15 ( flap

Vr = 105 MPH, Vy = 123 MPH

Soft and short field use 15 ( flap, crosswind use additional power with the upwind engine until the rudder becomes effective.

# FUEL

Usable fuel is 100 US Gallons (USG) in main tanks and 40 USG in auxiliary tanks.

23.8 USGPH @ 23”/2300 RPM @ 2500’ using normal lean mixture – TAS 196 MPH.

28 USGPH @ 24”/2450 RPM @ 2500’ using normal lean mixture – TAS 208 MPH.

Aircraft weighs 3 701 lb, usable fuel weighs 724 lb, leaving 875 lb for crew and baggage.

# APPROACH SPEEDS

Below 180 MPH with 15 ( flap and 160 MPH with gear down. 123 MPH with 15 ( flap and 108 MPH with 35 ( flap.

# UPPER AIR WORK AND STALLING SPEEDS

Vmc= 86 MPH (red radial)

Power off @ 5300 lb: 	Gear up and flaps up - 86 MPH.  Gear down and flaps 15 ( - 81 MPH.  Gear down and flaps 35 ( - 72 MPH

# GLIDE

Pilot’s Operating Handbook gives 111 MPH (aircraft covers 5 Nm from 2 500’ agl).

# SUCTION

5 ( 0.1 inches of mercury	www.gridline.co.uk 	22-Oct-00   G-REDB.doc