G–VECD ROBIN R 1180 T 1978

# TAKE OFF AND CLIMB

Vr = 65 kt, Vy = 75 kt		Normal take-off without flap

Vr = 65 kt, Vx = 70 kt		Normal take-off with 10 ( flap

Vr = 65 kt, Vx = 65 kt		Obstacle clearance with 10 ( flap

Soft and short field use 10 ( flap	Crosswind (22 kt limit) use 10 ( flap

# FUEL

Usable fuel is 60 US Gallons (USG)

9.3 USGPH @ 2400 RPM @ 2500’ using best power mixture – TAS 118 kt.

10.3 USGPH @ 2500 RPM @ 2500’ using best power mixture – TAS 123 kt.

Aircraft weighs 1 574 lb, usable fuel weighs 360 lb, leaving 601 lb for crew.

# APPROACH SPEEDS

84 kt with flaps up, 70 kt with 30( flap, crosswind use 20 ( flap and 75 kt.

67 kt with 40 ( flap crossing the threshold with power on for a short field landing.

# UPPER AIR WORK

‘U’ Category 2535 lb – stalls, steep turns, lazy eights, chandelles.

# STALLING SPEEDS

Power off @ 2535 lb: 	Clean - 63 kt.  Flaps 10 ( - 60 kt.  Flaps 40 ( - 52 kt

# GLIDE

Pilot’s Operating Handbook gives 75 kt (aircraft covers 2.9 Nm from 2 000’ agl).

# LIMITATIONS

Day VFR, in non-icing conditions, Class 3 radio fit	  10-Jun-01 G-VECD.doc